## Slide 1
SEMICON INDIA HACKATHON 2026
DRIFT-SENSE
Resilient Localization. Uncompromised Precision.
AI-powered navigation-error recovery for periodic semiconductor wafer inspection.
APPLIED MATERIALS
FINFET-STYLE
DEEP LEARNING
TEAM DETAILS:
S/N | NAME | ROLE | CONTACT | 
 |  |  | MOBILE | E-MAIL
1. | MANAS BAJPAI | TEAM CAPTAIN, AI/ML Engineer |  | vlsimcte@gmail.com
2. | SUKHVEER SINGH | DATASET ENGINEER | 8755700791 | rahulkumarnauhwar179@gmail.com
3. | BOREY DUTTA | TESTING & DEPLOYMENT | 8699615162 | dattaborey2@gmail.com
4. | SUDHEER CHOUDHARY | DATASET DEVELOPMENT | 8319795223 | Jat.sudhir6677@gmail.com
TEAM NAME: MCTE Team 2
COLLEGE NAME: MILITARY COLLEGE OF TELECOMMUNICATION ENGINEERING
MHOW, INDORE(M.P).

## Slide 2
02
Problem Statement Addressed
Drift-Sense: Navigation-Error Recovery
THE INDUSTRY PROBLEM
A wafer inspection tool must revisit the same site repeatedly with extremely high positional consistency. Small stage errors can accumulate through thermal expansion, vibration and mechanical slack. A revisit may land several pixels away from the intended site. The difficulty is not only drift: semiconductor layouts repeat. A wrong location can look almost identical to the correct one.
WHY TEMPLATE MATCHING BREAKS
Highly repetitive DRAM cell arrays create multiple visually similar locations. A conventional template matcher may therefore lock onto the wrong periodic copy instead of the intended site.
OUR OBJECTIVE
Given a reference image and a larger search image: 1. Find the intended pattern location 2. Suppress periodic false matches 3. Remain robust to independent sensor noise, blur, rotation and scale variation 4. Output one center coordinate: (x, y)

## Slide 3
03
Idea Description
DRAM-style synthetic layouts + AI-based localization
1 • ARCHITECTURE
DRAM-STYLE Synthetic patterns model repetitive DRAM memory-cell arrays, including:
Word-line-like structures
Bit-line-like structures
Repeated memory-cell patterns
Contact/storage-node features
Why DRAM?
Strong periodic structure
High visual similarity between neighboring cells
Naturally exposes periodic localization ambiguity
Suitable for testing robust navigation-error recovery
2 • LOCALIZATION
AI-BASED LOCALIZATION A shared feature encoder extracts structural representations from both images. Multi-scale correlation identifies candidate positions while preserving spatial context. A coordinate-refinement stage estimates the final (x, y) center with sub-pixel precision.
3 • WHY NOT TEMPLATE MATCHING?
Raw template matching is dominated by repeated local appearance. Drift-Sense instead combines: • Learned structural features • Multi-scale agreement • Candidate consistency • Coordinate refinement Goal: Identify the intended DRAM cell location—not simply the most visually similar location.

## Slide 4
04
Proposed Solution
Controlled synthetic data + periodicity-aware multi-scale localization
REFERENCE
Reference image
→
SEARCH
Search image
→
ENCODER
Shared feature encoder
→
MATCH
Multi-scale correlation
→
FILTER
Periodicity-aware candidate scoring
→
REFINE
Coordinate refinement
→
OUTPUT
(x, y)
DATASET GENERATOR
• DRAM-style periodic cell structures • Wordline/bitline-like repeating patterns • Randomized cell placement and pitch • Reference & search image size variation • Independent sensor noise • SEM-inspired edge brightening/contrast • Blur, rotation & scaling
Controlled variation allows the model to learn realistic localization uncertainty rather than memorize fixed patterns.
LOCALIZATION MODEL
• Shared-weight feature encoder • Multi-scale feature pyramid • Reference-to-search correlation • Candidate peak extraction • Periodicity-aware suppression • Final coordinate refinement Design principle: Use structural and contextual evidence across scales instead of relying only on raw pixel similarity.
ROBUSTNESS DESIGN
Training emphasizes variation rather than memorization. Test protocol: • ≥30 fresh randomized pairs • Higher search-image noise than training • Both easy and highly periodic regions • Report error distribution, tolerance accuracy and runtime This mirrors the official Applied Materials test intent [1].

## Slide 5
05
Innovation & Uniqueness
Designed around the actual failure mode: periodic ambiguity
01 Periodicity-Aware Scoring
Avoids the assumption that the highest local similarity is unique. Candidate locations are compared using structural and multi-scale evidence.
02 Independent-Capture Simulation
Reference and search images receive independent sensor noise, reflecting separate physical acquisitions.
03 SEM-Informed Image Formation
Edge-brightening is explicitly modeled because secondary-electron SEM images show characteristic bright edge contrast.
04 10× Scale-Aware Localization
The system is designed for the required reference/search scale relationship using multi-scale features and coordinate refinement.

## Slide 6
06
Results
Use measured results from the exact GitHub version submitted to i4C
TEST CASES
[30]
≤1 px ACCURACY
[100%]
≤3 px ACCURACY
[100%]
≤5 px ACCURACY
[100%]
MEAN ERROR
[0.0 px]
INFERENCE
[397.25 ms]
SUCCESS CASE — INSERT ACTUAL VISUAL
Reference image | Search image True center: (646,408) Predicted center: (646,408) Pixel error: [0.00 px]
Matching score : (0.9202)
Successful localization under rotation and scale variation. The proposed rotation-scale search followed by full-resolution verification correctly localized the DRAM target with zero pixel error.
HONEST FAILURE — INSERT ACTUAL VISUAL
Reference image | Search image True center: (154,813) Predicted center: (173, 522) Pixel error: [291.62 px] Failure caused by periodic structural ambiguity. The search image contained visually similar repeating DRAM patterns. The matcher selected a structurally similar distractor instead of the true target location. This failure motivated the final rotation-scale locked local verification approach.
Evaluation performed on the current 30-sample DRAM v2 evaluation set.

## Slide 7
07
Technology & Feasibility
Reproducible Python implementation with deployment-focused inference
SOFTWARE STACK
Python 3.14.2 OpenCV 5.0 NumPy 2.4.1 SciPy 1.17
Pandas 3.0.1 Matplotlib 3.9+ scikit-learn 1.8 Model export: PyTorch / ONNX (optional) CLI inference: standalone Python script
DEVELOPMENT HARDWARE
GPU: [Actual GPU] CPU: [Actual CPU] RAM: [Actual RAM] CUDA: [Version] Cloud: [None / Platform] Dataset generation: [~Few minutes / 30 samples] Training: [time] Model size: [N/A] Inference: [397.25 ms / pair]
FEASIBILITY & SCALABILITY
• Generator parameters expose architecture, noise and placement diversity. • Ground truth is generated automatically, enabling repeatable evaluation. • Inference is packaged as a single command for evaluator use. • The architecture can be extended from FinFET to DRAM-style layouts without changing the core coordinate-output interface.

## Slide 8
08
GitHub & Video Link
Mandatory reproducibility package
PUBLIC GITHUB REPOSITORY
Repository: https://github.com/dattaborey2-ai/Drift-Sense-Wafer-Inspection Required contents: • README.md • generate_dataset.py • inference.py ← critical evaluator script • train.py / notebook • model weights (.pt/.onnx) if DL • requirements.txt • ground_truth.csv / evaluation code • references / citation document • example input pair
EVALUATOR RUN
Dataset generation: python generate_dataset.py --architecture finfet --num_pairs 100 --output_dir ./dataset Inference: python inference.py --reference reference.png --search search.png Output: (x, y) No manual path edits, GUI steps or source-code changes.

## Slide 9
09
References
Use the same numbering in the PPT, README and citation document
[1]
i4C / SEMICON India Hackathon 2026 — Drift-Sense problem statement and submission requirements.
Official
[2]
Villarrubia, J. S. et al. (2001), “Edge Determination for Polycrystalline Silicon Lines on Gate Oxide,” NIST / SPIE.
SEM edge
[3]
ETH Zurich ScopeM, “SEM – Imaging with Secondary Electrons.”
SEM edge
[4]
Microelectronic Engineering (2019), “Deep learning denoising of SEM images towards noise-reduced LER measurements.”
SEM noise
[5]
Szeliski, R., Computer Vision: Algorithms and Applications, Springer.
CV
[6]
Lowe, D. G. (2004), “Distinctive Image Features from Scale-Invariant Keypoints,” IJCV.
Scale/registration
[7]
Oxford Academic, “Spatial resolution in secondary-electron microscopy.”
SEM imaging